## Slide 1
DECENTER - overview
Date: 30/08/2018
Authors: Vlado Stankovski & DECENTER Project Partners
Notes: 1

## Slide 2
Content
General principles
Requirements analysis
Structural views
Process views
Deployment views
Testbed
Relationship to SOTA
Software resources
2

## Slide 3
General Principles
Decentralization
  promote P2P with Client-side application management
  in favour of Federated Cloud, Multi-Cloud, etc.
Enable minimum number of technical use cases that can:
  expand to all scenarios; and
  exploit and demonstrate DECENTER’s platform benefits
Enable minimum number of system components and application
descriptors: application descriptor, orchestrator, Fog Exchange,
Local Scheduler, life-cycle manager
Build from the simplest software stack
3

## Slide 4
Applications as Technical Use Cases: Definition
Technical use cases will represent our intended applications:
  I. VIDEO BASED USE CASE:
    Several video streams need to be analysed with AI models
    Goal: detect potential danger situation
  II. SENSORS BASED USE CASE:
    A network of various sensors periodically collect data from surroundings
    The collected data needs to be processed
    Goal: optimise energy consumption
  Second step, cascading, I and II merge for second stage
Let us design potential architecture for both applications
4

## Slide 5
Technical Use Cases: Common Architecture
5
Three major components:
  Video/Data Stream Collector
  Video/Data Stream Buffer
  Video/Data Stream Processor
Stream-processing architecture:
  Can handle massive quantities of data
  Provides views of online data

## Slide 6
Technical Use Cases: Architectural Components
6
Stream Processor
Subscribes to the Stream Buffer to a stream of records
Applies pre-trained AI model to individual frames/sensor data
Produces prediction/classification results
Example technologies: Apache Spark/Flink with ML library
Stream Collector
Receives stream from IP cameras or IoT devices
Converts video stream into a sequence of decompressed frames
Publishes extracted frames or IoT data on Stream Buffer
Examples: ?
Stream Buffer
Publish-Subscribe queue of events with temporal and visual/sensor data
Examples: Apache Kafka, AWS Kinesis, GCP Dataflow, Azure Stream Analytics

## Slide 7
Technical Use Cases: Discussion
7
Remarks
Both technical use cases employ the same architecture.
The AI models (Stream Processors) can employ either data (supported in e.g. TensorFlow) or model distribution (more complex).
Potential issues
Decompressed video can impose high bandwidth requirements:
Mbps

## Slide 8
Applications: Architectural Requirements
The architecture should meet the following goals:
  Loose Coupling, Fog (Peer) Nodes
  Scalable design, data/process should be distributed over at least few Peers to achieve vision of Fog
  Disposable resources
  Automation
  No single point of failure?
  Works for Big Data
  Should operate in real-time
  Support the use of AI methods
  Support AI training
8

## Slide 9
Architectural styles
  Master-Slaves
  Every peer can be Master or Slave
Fog Peer - Master
Fog Peer - Slave
Fog Peer - Slave
Fog Peer - Slave
Service delegation
Service delivery
Client
9

## Slide 10
Architectural styles
  Dedicated backend with orchestration functionality
  Add classical Cloud to this picture
Heavier, dedicated frontend/backend for each specific smart application with Brokering (Fog Exchange) for QoS monitoring, decision making, and orchestration capability
Fog Node
Client
Resource access
Service delivery
Fog Node
Fog Node
10

## Slide 11
Structural views
  How to arrive to the main entities and structure?
  First stage, technology agnostic, keep technologies in mind
  Put every entity deemed necessary on the grand canvas – collaborative effort needed
  Provide one slide text description of every proposed entity and its function
  We aim at clear separation between application services and the Fog Computing Platform services
  Generally three areas:
    Fog Exchange (Broker) – analogy to crypto exchanges, partners in T3.2, broker…
    Fog node – consider reference CNCF.io and Open Fog Consortium architectures
    User and application side – every deployment can be unique deployment
    Supporting entities: container images storage, metadata sharing and management, data storage, if necessary
  Discuss and decide where the component fits it in the architecture
  Which are minimum necessary components for early prototype
11

## Slide 12
Switcher, Scheduller, Load Balancer
Information Manager (QoS, Security, Policies)
Metadata Management
Video input distributor
Sensor input distributor
Decision Maker
Supply and Demand Manager
Application:
Application descriptor
QoS model
Orchestrator
Web application: training view
Web application: AI view
AI operation - 1
Proxy transcoder – AI training
AI operation - 2
QoS Monitoring
Metadata Management
Application Descriptor
Object storage: data and container images
Backend
Container Images Delivery, Deployment, Management
Master Fog Node Access Control
Replica (Slave) Fog Node Access Control
Data Manager
Containers IPs and ports management
Client
12
Multicasting
AI operation - 3
AI operation - 4
Fog Computing Exchange
BC & SC
Fog Broker Mechanisms:
Functionalities, Smart Contracts, on-chain and off-chain metadata management

## Slide 13
How to describe potential functional components? See the following
13
  Explain what is the functionality
  Explain what arguments it should take
  Give an idea of the methods that have to be implemented
  Provide examples on how to use it
  Some examples to stimulate thoughts are provided

## Slide 14
Input distributor for video-streams
The purpose of the Input Distributor is to provide uncompressed essence in specifics multicast addresses, following the NMOS standard.
This way, we ensure interoperability when transferring essence between the containers.
Can receive MPEG Transport Stream (TS), packetized in Real-time Transport Protocol (RTP).
For our scenario, the TS have only one program with two essence streams:
Video: AVC - block-oriented motion-compensation-based video compression standard
Audio: ST302M (PCM audio in TS).
Can handle streams with multiple video resolutions.
Possible arguments for Docker based service: Listen port (RTP+RTCP), Output Multicast Address, Output Multicast port, Waiting time, Video Width, Video Height
How to access? The service expects at given port MPEG-TS over RTP.
Testing: ffmpeg to feed the Docker container
For example, if the file has video essence with H.264, we can use:
ffmpeg -i <input file> -vcodec copy -acodec s302m -strict 2 -tune zerolatency -f rtp_mpegts rtp://<multicast ip>:<port>?pkt_size=1316
14

## Slide 15
Proxy transcoder for video-streams
Transcoding is the ability to adapt digital files so that content can be viewed by the user for training purposes.
The purpose of the Proxy Transcoder is to provide a low resolution coded stream of one uncompressed stream.
With this, the resources required to handle the monitoring stream are much more reduced.
Receives video uncompressed packetized in RTP (NMOS).
Sends out MPEG-DASH video stream.
Possible arguments for Docker based service: Listen port, Multicast Address, Output port (80), Video Width,
Video Height
Expects Uncompressed video packetized in RTP (RFC 4175)
Sends out DASH segments and a MPD file
15

## Slide 16
Switcher for video-streams – if needed?
The purpose of the Switcher is to select specific input streams based on an event, to be fed into specific AI method. Several input, just one output.
Receives multiple videos, uncompressed and packetized in RTP (NMOS).
Sends out RTP (NMOS) video stream.
Possible arguments for Docker based service: Channel A - Listen port, Channel A - Multicast Address, Channel B - Listen port, Channel B - Multicast Address, Waiting time, Output Multicast Address, Output Port, REST Port,
Video Width, Video Height
To switch video streams:
Send a POST request to http://[HOST_IP]:[switcherREST]/switch with:
Header: Content-Type: application/json
Payload: {"camera": 1} for camera 1 or {"camera": 2} for camera2
Server will answer 'OK' (200) if successful.
16

## Slide 17
Distributed computing (viewpoint)
  AI methods: (1) training is supported?, (2) using
  Application architectures:
    Bag of tasks, gangs, which one is it appropriate?
    DAGs, workflows (are probably) out of scope?
  Persistent and in-memory data management requirements of the AI methods, which ones are required?
17

## Slide 18
Bag of tasks
AI method A
AI method A
AI method A
AI method B
18
  Is any data pre-processing needed? E.g. input stream partitioning? Is every video stream linked to just one process?

## Slide 19
Gangs: continuous inter-process data exchange
AI method A
AI method A
AI method A
AI method B
19

## Slide 20
Elasticity events
20
AI method A
AI method A
AI method A
AI method D
AI method B
AI method C
  What triggers scaling (elasticity)?
    Detected events in the environment?
    Attaching more cameras or sensors?
    Adding more of the same AI methods?
    Increasing resolution?
    Adding more (or different) AI methods to the same input streams?
    Big Data storage requirements? Objects, structured data!?

## Slide 21
Devices and data communication formats
  Examples of specific video streaming protocols
  Examples of specific sensor data streaming protocols
  Possibility to develop a script which uses existing videomaterial for training and to simulate large number of cameras and sensors
  Example, is https://www.ffmpeg.org/ useful? If not suggest other tools
  May we proceed with development regardless of the actual physical setting based on ffmpeg testing case?
21

## Slide 22
Fog Exchange (Broker) API design
  Smart Contracts implementation
  Technology biased
  What functionalities will be provided:
    Supply?
    Demand?
    QoS verification?
    Monetization of services?
    Orchestration based on TOSCA OASIS descriptor?
  Make a wish list of Fog Exchange (Broker) related actions
  Need to shortlist technologies: Ethereum, Cardano, Tron, EOS
22

## Slide 23
Cloud object storage;
container images storage
Initial off-chain metadata exchange system (off-chain)
Smart Contracts APIs:
Application descriptor
Peer node
Peer APIs:
Client
BLOCKCHAIN SERVICES
Fog Exchange
APIs:
Peer node
Peer APIs:
Client
Client
APIs
23
The Fog Exchange viewpoint

## Slide 24
Process views
  How should the key technological components communicate? High-level overview and separation of concerns is needed.
  What information shall they exchange?
  What formats will data and metadata take?
  Start with application descriptor?
  Provide example for each intended application.
  Let‘s draw few basic examples
24

## Slide 25
Application descriptor and metadata management
Pre-steps:
  A DevOps prepares application descriptor / manifest:
    Application components definition (e.g. as in TOSCA)
    Components relations (e.g. as in TOSCA)
    QoS requirements (additionally to TOSCA)
    Privacy concerns, i.e. which components are restricted to Fog (additionally to TOSCA)
Decide how, where to store metadata about the application, also for runtime management?
25

## Slide 26: AI model optimization methods
Pruning: need to decide which network to be pruned
Parameter Quantization: Degrades accuracy
Design from Scratch: hard to be applied to pre-trained network
Network Partitioning
Ko, Jong Hwan, et al. "Edge-host partitioning of deep neural networks with feature space encoding for resource-constrained internet-of-things platforms." In AVSS, 2018.
H. Yonekawa, S. Sato and H. Nakahara, "A Ternary Weight Binary Input Convolutional Neural Network: Realization on the Embedded Processor," 2018 IEEE 48th International Symposium on Multiple-Valued Logic (ISMVL), Linz, 2018, pp. 174-179.
Han, Song, Pool, Jeff, Tran, John, and Dally, William J. Learning both weights and connections for efficient neural networks. In Advances in Neural Information Processing Systems, 2015.

## Slide 27: Network Partitioning
Partitioning of an AI model
  Divide a neural network
  Save partial networks to separate models
  Deliver intermediate data between them
Pros and cons of AI model partitioning
  Pros: Smaller device computing resources comparing to the original model
  Cons: One additional transmission of intermediate data
Delivery of Intermediate Data
  The output of the previous neural network needs to be transmitted to the input of the next neural network.
  Protocol for this intermediate data transmission
Intermediate Data
VGG16 : 5 Convolution Layers+ 3 Fully Connected Layers
VGG16-CV : 5 Convolution Layers
VGG16-FC : 3 Fully-Connected Layers

## Slide 28: Compression of the Intermediate Data
Consideration on the Intermediate Data
  Intermediate data size depends on the layer where division occurs
  If that layer has many neurons, intermediate data size will increase
  Small model size does not guarantee faster computation
   Need special care on selection of division point.
Proposes a novel Intermediate Data Compression Method
  To reduce the effect of intermediate data transmission
  Keep AI model as it is, compress intermediate data instead
 | Original Intermediate Data Size | Modification in activation function | Final compression result
Feature size | 4,377 KB | 2,799 KB | 598 KB
Data type | Float 32 | Float 32 | UINT8
<Example of Intermediate Data Compression>
<Size of Intermediate Data of Yolo v3>
Notes: Emphasize novelty of this compresiion method.

## Slide 29: Implementation and Test Results
<Partitioning of VGG16 for image classification>
<Partitioning of Yolov3 for object detection>
. Original model size : 528 MB
. Front model size : 57 MB
. Rear model size : 472 MB
. Intermediate data size : 100 KB
. Compression method applied : No
. Accuracy Loss : No
Original model size: 236 MB
Front model size: 154 MB
Rear model size: 82 MB
Intermediate data size: 596 KB (Original size: 4,377KB)
Compression method applied: Yes
Accuracy Loss: Yes
Single Instance | First Edge (ConvNet) | MQTT | Second Edge (FC-Net)
436 | 350 | 112 | 56
406 | 380 | 120 | 45
427 | 400 | 108 | 76
435 | 402 | 136 | 54

## Slide 30: Nomenclatures for AI application service architecture
AI Model | A trained model (either a deep neural network or other ML).
AI Method | An entity serving the inference of a trained model (runs the model on the ML engine).
AI Service | An entity serving a certain AI function (model serving layer) based in an AI Method.
AI App | An entity invoking AI Methods to provide AI functionalities to the end user.
AI Application Service | An entity which consists of set of AI functionalities delivered to an end user.

## Slide 31: DECENTER Reference Architecture – Functional View
Data Preprocessor
Data Postprocessor
IoT Platform
AI App
AI Service
AI Application Service
AI Model
app request, device URL
detection/prediction/insight
User
Devices
IoT device information and control
IoT Protocols
AI Method

## Slide 32: Trust as a High-Level Requirement in Fog Computing
Developed proof-of-concept scenarios1:
SOTA analysis for trust management in fog computing including data management
Explore Off-chain and On-chain data related trust attrtibutes
Registration of participants (users and providers) for transparency and traceability
Trusted access to decentralised data resources including cameras (video streams)
Traceability of the data flow among the resources (camera, Fog, Cloud) with regard to security and privacy preservation requirements
Different smart contract template designs among the entities that involve the use of Smart Oracles
Currently used for the design of the cross-border data management approach of task T4.3
1 Trust Management in a Blockchain Based Fog Computing Platform with Trustless Smart Oracles
Kochovski et al., Trust management in a blockchain based fog computing platform with trustless smart oracles, FGCS, Vol. 101, 2019, pp. 747-759.

## Slide 33: Data Model Management Structure
Trusted Model Manager
Event/ Trigger
Korean regulation
EU regulation
Smart Oracle
BlockChain Service
ETH node
Resource Selector
Orchestrator
AI Model Repository
Data Management
DECENTER Platform
External Data
API
BC
SmartContract Template
Smart Contract
Trusted External Data
Request Verification
Verification
Result
Data Management
AI Service deployed on k8s cluster
AI model injection

## Slide 34: Highly-Regulated, Transparent, Traceable AI Model Management
BC
Remote
Platform
Home
Deployment
Configuration
Trusted Model Manager
Blockchain Service
AI Model Repository
Data Management
Ethereum PoW
AI Container
Smart Oracles
App. Serv. provider
AI Model
Deployment Request
Resource Selector
Deploy
AI Model
PushAIModel
Completed
Verification
(configuration, permissions)
SC Template
DeploySC(details)
Regulations
Certificates
Permissions
AI Model
Deployment Request
Request model
from AI Model
Repository
DeploySC(details)
AIModelDeploy
Consensus PoW
Wait for Verification

## Slide 35: AI Model Description and its Repository
<Description Schema for AI Model>
- XML Schema
model_information: general information
partial_information: whether and how a model is partitioned.
train_information: information of training environement
<Preliminary implementation of AI Model Repository>
AI Model Repository
RESTful API to access specified AI Model
Notes: JW’s work

## Slide 36: Resource Models
Model:
  Fog infrastructure resources
  Topology of AI application
Main existing standards:
  OCCI
  OASIS TOSCA
Notes: Take inspiration
Existing works do not focus on fog/edge
We are evaluating and discussing with other European projects to see if we can contribute to OASIS TOSCA

## Slide 37: Model of Fog Infrastructure Resources
Describe Cloud-to-Things resources (Comp.Res., Host, Thing)
Support federation (Adm.Domain, Region, Connection)
Enable resource sharing (adv., reservation, acquisition; Res.Collection, Price)
Notes: The components in the object diagram are as follows. An Administrative Domain represents an entity that owns a distributed Fog infrastructure. An infrastructure that is owned by a single Administrative Domain is geographically located in one or more Regions and is ideally spanned over the whole Cloud-to-Things continuum. A Connection models a link between any two infrastructures belonging to either the same or different Administrative Domain that reside in different Regions. This allows to describe federated resources in both vertical and horizontal directions.
Each infrastructure in a Region constitutes a set of computational Hosts and optional External Endpoints. A Host represents a physical or virtual machine that essentially consists of a set of Computational Resources, which are Processor, Memory and Storage. A processor can be further distilled into CPU, representing central processing unit, and GPU, representing graphics processing unit. Some providers might offer a pre-configured bundle of virtual resources. These can be described with an Image, which represents machine’s disk, and Flavor (in Cloud domain more known as instance type), which describes a set of virtual resources that constitute a virtual machine. A Host and each of the individual Computational Resources can be attached a Price tag. This model of computational resources is therefore suitable for resource sharing.
External Endpoints that can be attached to a Region can represent either an External Service, such as remote database, or a Thing, such as sensor or actuator connected to the Internet.
Each Host provides a set of Metrics that are periodically collected through a monitoring system. Moreover, a Host can be shared with infrastructure belonging to another Region for a given Price while guaranteeing that an associated SLO (Service-Level Objective) is met. Collected metrics allow to measure whether a defined SLO is guaranteed or not.
Finally, Hosts can run zero or more Microservices, each representing the Application components.

## Slide 38: Model of Fog Application Resources
Describe application as a DAG of linked components
  Microservices
  External endpoints
  DataFlows
Notes: On a Host, an Application can be deployed in terms of its constituting Microservices. The diagram shows its decomposition into Microservices and DataFlows. The orchestration and deployment processes can take advantage of this model to determine the hosts where the different microservices shall be deployed, considering the requirements imposed on the computational resources (by the Microservices) and on the network resources (by the DataFlows).

## Slide 39: Service Level Agreements
Design QoS models for :
  Software services, Fog platform and infrastructure
  AI applications
Main existing standards:
  WSLA (IBM)
  WS-Agreement (OGF)
  OCCI (SLA)

## Slide 40: Service Level Agreement Template
Based on CSLA and WSLA
Main parts:
  Validity
  Stakeholders
  FogServiceDefinitions
  SLOs
  Billing
  Termination

## Slide 41: Service Level Agreement Template
FogServiceDefinitions:
  shall describe any service type (XaaS)
  IaaS and SaaS required for DECENTER

## Slide 42: Service Level Agreement Template
SLA parameters
  specify parameters to be used in SLOs
  specify metrics in relation to parameters
  metrics can be simple or composed
Notes: check graph

## Slide 43: Service Level Agreement Template
Guarantees
  A set of SLOs
  Preconditions
    optional
    restrict region and/or tier
  SLOs
    mandatory
    thresholds for SLA parameters
    can define confidence and fuzziness

## Slide 44
Thank you !